## Slide 1: Meet Teem
Alex Gonzalez, Ben Harker, Kyle Wahlberg

## Slide 2: An age old question:
Let’s talk about that

## Slide 3: The idea
We decided to model grilling and searing meats (assuming square cuts of even thickness)
After a detailed planning session, we made a GUI
Used diffusion equations for conduction and convection
Beef quark?

## Slide 4: The goal
Create a model for cooking meat
Currently only beef (but others could easily be added)
Choose how well done: rare, medium rare, medium, medium well, or burnt
Choose cooking method: grill or cast iron pan
Burnt

## Slide 5: The papers
Referenced two papers:
One outlining equations to use
One to find thermal constants for meat

## Slide 6: The math
NOT steady state solution
Use FTCS with boundary condition
Temperature set at 450 for grill grate, 400 for grill air, and 450 for cast iron
Insulate elsewhere

## Slide 7: Why not a different method?
FTCS model deals with diffusion in medium
Initially tried steady state equation for conduction from paper
But, we didn’t want a steady state solution. We needed it to be time dependent, and so FTCS was the answer.

## Slide 8: The numbers
For “Beef, lean, eye of loin, U.S. good grade”:
K = 0.185 BTU / (hr ft ℉) at 42℉
C = 0.56 BTU/(lb ℉)
𝛒 = 0.033 lb/ci
So 𝝟 = K / (c 𝛒) = 0.834 in2/hr
Convert to per in. and BTU / sec.

## Slide 9: The program
Iteratively solve for temperature at half the thickness
Shows time to cook per side
Set constants
Demo!

## Slide 10: More program
2D FTCS method
Slow plotting, but we need tau small enough to not go crazy
Didn’t try to model heat loss to atmosphere

## Slide 11: The GUI

## Slide 12: Credits:
All images copyright www.google.com/images 2019.